## Slide 1
Optimal Placement of EV charging stations in context of Indian urban networks
Analysis and Approach in context of Indian cities

## Slide 2
Problem Statement
Optimally deciding the location of EV charging stations in Indian cities taking into consideration various factors like charging facility investments, range anxiety, electrical network, road plans, etc.
Planning will involve :
EV charging station planning in distribution system and renewable resources integration
1
EV charging station planning in transportation network
Planning catering to uncertainities like driving behaviours,coordinated charging strategies,control systems etc.
2
3

## Slide 3
Solution Approach
Stage 1
Screening of the candidate locations for placement of charging station
Stage 2:
Optimization
The second stage aims at finding the no. of charging stations that could be paced at a particular place
MULTILEVEL- MULTI OBJECTIVE FUNCTION FORMULATION

## Slide 4
Stage 1
Screening of the candidate locations for placement of charging station
Parent nodes:congestion,VSF,Distance,reliability index
Child node: Candidate
Distance between node of the road network and nearest bus of the distribution network
Traffic intensity
Voltage stability index

## Slide 5
Stage 2
Optimization
01
02
COST
WAITING TIME
Determines optimal capacity of the charging facilities and charging demand during a time interval

## Slide 6
Test network
33 Bus distribution network+ 25 node transport network
Candidate locations :
3,5,6,7,19,22,24
Number of charging stations that could be placed at each location: 4

## Slide 7
Case study
Urban Area+highways :Chandigarh city
Candidate locations:
1,8,10,15,17,23,25,26,27,28,29,32,34,37,42,47,55,63,65,66
Number of charging stations at each node: Atmost 7

## Slide 8
Novelty
1
2
3
Novel approach
multi-stage multi-objective model : incorporates distribution system and transportation system constraints
takes care of installation + incurred costs
Cost Effective
best solutions as per energy demands and satisfactory approach using renewable resources and hydrogen cell ev stations if needed
Renewable resourcesintegration could be done

## Slide 9
FUTURE SCOPE
DG installation along with microgrids
models considering market scenarios
V2G integrations
Development of models for intterconnected cities

## Slide 10
Thankyou